## Slide 1: MEDUSA Methane Engine Design for Unmanned Small Aircraft
Test Readiness Review
University of Colorado at Boulder
03/05/2015
Customer: Dr. Ryan Starkey Advisor: Dr. Jelliffe Jackson
Team
Daniel Frazier Nathan Genrich Abram Jorgenson
Christopher Jirucha Crawford Leeds Huikang Ma
Alexander Truskowski Carlos Torres Corey Wilson
Notes: Good afternoon everyone, we are the MEDUSA team. Thank you for joining our pdr review

## Slide 2: Outline
Overview
Schedule
Testing
Budget
Project Overview and Schedule | Corey Wilson
Mechanical | Daniel Frazier
Software and Electronic | Crawford Leeds
Budget | Crawford Leeds
Project Overview
Mechanical
Software and Electronic
Budget
Engine Integration
Notes: I will start this presentation with the project description and baseline design. I will then pass it off to my colleagues to discuss the feasibility analysis for each of the critical element which including engine control unit, fuel delivery system and combustion can. I will then finish by providing a project summary

## Slide 3: Project Statement
Project Description: Modify a JetCat P90-RXi mini turbo jet engine to run on gaseous methane fuel to address the USAF’s interest in the possible use of the methane gas as fuel.
Functional Requirements | 
Engine Control Unit (ECU) | Start, run, and shut down engine Maintain JetCat recommended safe operation conditions Log data
Fuel Delivery System (FDS) | Deliver up to 4.2g/s of methane to combustion can Deliver kerosene/oil mix to bearings at stock rates
Project Overview
Mechanical
Software and Electronic
Budget
Engine Integration

## Slide 4: PROJECT OVERVIEW
Notes: This is our baseline design

## Slide 5: Project CONOPS and Objective
Current Stock Engine: JetCat P90-RXI
JetCat ECU
Injection point
Lubrication Line
RPM and Temperature from Engine Sensor Board
Kerosene
Fuel/Lubricant
Commands to pump/solenoids
RC Signal
RPM < 130,000
Exhaust Temp < 700oC
RC Receiver
Shaft

## Slide 6: Project CONOPS and Objective
Mass Flow Controller
Pressure Regulator
Safety Valves
Six Student
injectors
Methane Tank
Student ECU
Student Engine Board
RPM < 130,000
Exhaust Temp < 700oC
RPM and Temperature from Engine Sensor Board
Commands to pump/solenoids
Commands to Controller
Fuel Manifold
Use stock lubrication hardware
Will use stock sensors

## Slide 7
Fuel Pump
Kerosene Tank
Lubrication System
Mass Flow Controller
Fuel System
Methane Tank
Engine
Combustion Can
Turbine
Compressor
Nozzle
ECU
Throttle Command
RC Controller
Starter
Motor
Key
Physical Contact
Electrical Signal
Data
Provided
Purchased
Designed
Bearings
PWM
PWM
RS-232
0.9 - 4.2 g/s
PWM
Injectors
Cold Junction Compensation & Amplification
T5 < 700oC
Injectors
Lubrication Solenoid
Hall Effect Sensor
0-2500 Hz
Receiver
ESB
SPI
Logic Algorithms
Command Outputs
Input Receivers

## Slide 8: Critical Project Requirements
Requirement | Subsystem | Description
CPR.1 | FDS | The FDS shall deliver 0.9-4.2g/s ± 5% of methane to the combustion chamber
CPR.2 | FDS | The FDS shall deliver lubricant to the bearings at rates equal to or greater than stock rates
CPR.3 | ESB | The ESB shall read data from the existing thermocouple and hall effect sensor
CPR.4 | ESB | The ESB shall transmit sensor data to the ECU
CPR.5 | ESB | The ESB shall drive signals to engine hardware components
CPR.6 | ECU | The ECU shall implement open loop control to control fuel flow rate
CPR.7 | ECU | The ECU shall shutdown the engine should the exhaust temperature exceed 700oC or the RPM exceed 130,000
CPR.8 | ECU | The ECU shall detect an ignition failure, shutoff fuel flow, and drive compressor
Project Overview
Mechanical
Software and Electronic
Budget
Engine Integration
Notes: This slide is temporary. Just for verify the critical project requirement

## Slide 9: SCHEDULE
Project Overview
Mechanical
Software and Electronic
Budget
Engine Integration
Notes: This is our baseline design

## Slide 10: MEDUSA Current Work Plan
Electrical
Software
Labview
ECU Integration
Fuel Delivery
Lubrication
Engine Integration
Where We Are
MSR
ECU Phase I (Completed):
ECU & ESB: Finished both prototypes, passed functional tests
Software: Individual functions complete
Simulator: LabView code complete and verified.
ECU phase I (Completed)
ECU phase II
ECU phase III
FDS phase I (Completed)
FDS phase II
SFR
TRR
Week 10
Week 12
Week 14
Final system Test
ECU Phase II (In progress):
ECU & ESB Board manufacturing
ECU hardware & software Integration
Engine simulator test - verify ECU requirements
ECU Phase III:
ECU& ESB Board revision manufacturing if necessary
ECU and ESB board verified for engine integration
FDS Phase I (Completed):
FDS components ordered, received and manufactured
FDS Phase II (In progress):
FDS seal and flow rate verification test
Lubrication flow rate date collection test
Final System Test:
Integrating ECU and FDS with engine
Mock engine test with hardware
Methane engine test run – validate the project requirments
Spring Break

## Slide 11: Testing Architecture & Presentation Layout
Fully integrated engine test
Engine simulation with Labview
ECU/ESB Integration
Seal & Flow
Rate Checks
Lubrication Flowrate Data Collection
ECU/ESB
Chip Tests
ECU Function Development
Level 1
Drive mechanical components with ECU/ESB
Mock engine test with hardware
Level 3
Level 2
MSR
TRR
Spring Break
April 20
Electrical
Software
Mechanical
Verification Test
Engine Functions With Methane
Project Overview
Mechanical
Software and Electronic
Budget
Engine Integration

## Slide 12: Testing Architecture & Presentation Progress
Fully integrated engine test
Engine simulation with Labview
Mock engine test with hardware
ECU/ESB Construction
Seal & Flow
Rate Checks
Lubrication Flowrate Data Collection
ECU/ESB
Chip Tests
ECU Function Development
Level 1
Drive mechanical components with ECU/ESB
Level 3
Level 2
MSR
TRR
Spring Break
April 20
Electrical
Software
Mechanical
Verification Test
Engine Functions With Methane
Seal & Flow
Rate Checks
Project Overview
Mechanical
Software and Electronic
Budget
Engine Integration
Notes: This is our baseline design

## Slide 13: Methane Delivery: Flow Rate Verification
Run Engine With Methane
Deliver methane from
0.9 - 4.2 g/s (Idle to Full Thrust)
Meet flow rate command within 5%
Must validate system and predictive models
Pressure vs Flow Rate Flow rate vs Temp
CPR.1
CPR.1
Project Overview
Mechanical
Software and Electronic
Budget
Engine Integration

## Slide 14: Methane Delivery: Seal Verification
Goal: Verify system has leak rate below 4% of commanded flow rate
125 PSI (Maximum operational pressure)
Mass Flow Controller
Fuel Injectors
Air Compressor
Pressure Gauge
Safety Valves
Check Valve
Performed with air at Boulder Municipal with a blast tunnel
5% total mass in tubes
Jan 30 8hr Remain Mar 10
Equivalent methane leak within OSHA standards

## Slide 15: Methane: Pressurized Delivery Verification
Mass Flow Controller
Fuel Injectors
Pressure Vessel
Relief Valve at operational engine pressure
Manual Control
0.9-4.2g/s
Flowrate Delivered
Safety Valves
Fan Disperses Methane
Error < 1% of Commanded Rate
Check Valve
Goal: Verify systems delivers methane within 5% of commanded rate (CPR.1)
Performed with air at Boulder Municipal with a blast tunnel
Air Compressor

## Slide 16: Methane: Pressurized Delivery Verification
Mass Flow Controller
Fuel Injectors
Pressure Vessel
Relief Valve at operational engine pressure
Manual Control
0.9-4.2g/s
Flowrate Delivered
Safety Valves
Fan Disperses Methane
Total Delivery Error < 5% Commanded
Mar 4 10hr Remain Mar 15
Check Valve
Leak Error from controller to injectors
Command Error
Goal: Verify systems delivers methane within 5% of commanded rate (CPR.1)
Performed with air at Boulder Municipal with a blast tunnel
Air Compressor

## Slide 17: Testing Architecture & Presentation Progress
Fully integrated engine test
Engine simulation with Labview
Mock engine test with hardware
ECU/ESB Construction
Seal & Flow
Rate Checks
Lubrication Flowrate Data Collection
ECU/ESB
Chip Tests
ECU Function Development
Level 1
Drive mechanical components with ECU/ESB
Level 3
Level 2
MSR
TRR
Spring Break
April 20
Electrical
Software
Mechanical
Verification Test
Engine Functions With Methane
Lubrication Flowrate Data Collection
Project Overview
Mechanical
Software and Electronic
Budget
Engine Integration
Notes: This is our baseline design

## Slide 18: Lubrication: Experimental Test
Run Engine With Methane
No documentation, determine experimentally
Will use stock rates, but these are unknown
CPR.2
Lubricate bearings to prevent seizing
Project Overview
Mechanical
Software and Electronic
Budget
Engine Integration

## Slide 19: Lubrication: Experimental Test
Lubrication Solenoid
Fuel
Solenoid
Bearings
Injectors
Fuel Can
Pump
1
2
Flowmeter
Flowmeter
1
2
Bearing
Lubrication
Goal: Find flow through Lubrication Solenoid
On Hold because of weather
Jan 20 5hr Remain Mar 14
Performed with kerosene at Boulder Municipal with a blast tunnel

## Slide 20: Lubrication: Calibration & Error Test Results
Fuel Can
Pump
1
2
Flowmeters
1-3V Power Supply
Filter
Goal: Calibrate flowmeters and calculate test error
Relative Flowmeter Error
Performed in Dr. Starkey’s lab with fire extinguisher
1
2
250ml Graduated Cylinder
Pulses/Quantity=Calibration Factor
 | Omega 601b | Equflow 0045
Tested | 29000 | 116000
Manufacturer | 36000 | 110000

## Slide 21: Lubrication: Calibration & Error Test Results
250ml Graduated Cylinder
Fuel Can
Pump
1
2
Flowmeters
1
2
Error
1-3V Power Supply
Filter
Goal: Calibrate flowmeters and calculate test error
Calibration Error
Relative Error
Performed in Dr. Starkey’s lab with fire extinguisher
Pulses/Quantity=Calibration Factor
 | Omega 601b | Equflow 0045
Tested | 29000 | 116000
Manufacturer | 36000 | 110000

## Slide 22: Lubrication: Calibration & Error Test Results
250ml Graduated Cylinder
Fuel Can
Pump
1
2
Flowmeters
1-3V Power Supply
Filter
Goal: Calibrate flowmeters and calculate test error
Jan 20 10hr Remain Mar 14
0.07mL/s
2% of Max Achievable Throttle
0.001±0.046mL/s
Performed in Dr. Starkey’s lab with fire extinguisher
0.014±0.011mL/s
45 Tests, 6 most refined procedures
Calibration Error
Relative Error

## Slide 23: Lubrication: Remaining Work
Complete Engine Testing
Analyze data
Prove ECU can operate lubrication system (CPR.2)
  Drive pump with ECU
  Check flow rate produced
  Test in Dr. Starkey Lab with
  fire extinguisher
Predicted 30 hours, has taken 60 so far
  15 hours to go
  Not a scheduling problem
250ml Graduated Cylinder
Pump
ECU
Filter
Lubrication Solenoid
Engine Lubrication Tubing

## Slide 24: Testing Architecture & Presentation Progress
Fully integrated engine test
Engine simulation with Labview
Mock engine test with hardware
ECU/ESB Construction
Seal & Flow
Rate Checks
Lubrication Flowrate Data Collection
ECU/ESB
Chip Tests
ECU Function Development
Level 1
Drive mechanical components with ECU/ESB
Level 3
Level 2
MSR
TRR
Spring Break
April 20
Electrical
Software
Mechanical
Verification Test
Engine Functions With Methane
ECU Function Development
Project Overview
Mechanical
Software and Electronic
Budget
Engine Integration
Notes: This is our baseline design

## Slide 25: Software/Electronics: Command Testing
Engine Control Unit
Engine Control Unit
Engine Sensor Board
Test functionality without risking engine damage
Control engine state
Check safety conditions
Run Engine With Methane
CPRs. 3-8
Project Overview
Mechanical
Software and Electronic
Budget
Engine Integration

## Slide 26: Electrical/Software: Command Flow
Raw
Sensor Data
Student Engine Sensor Board
(ESB)
Methane Delivery System
Stock Engine Components
Component Commands
RC Command
Student Engine Control Unit
(ECU)
Processed
Sensor Data
Processed Data
Command
Component
Key
Raw Data

## Slide 27: Electrical/Software: Command Flow
Thermocouple
RPM Sensor
Student Engine Sensor Board
(ESB)
Starter Motor
Pump
Solenoid
Glow Plug
Methane Delivery System
Combustor
RPM
TEMP
Starter Motor
Pump
Solenoid
Glow Plug
Flow Control
Student Engine Control Unit
(ECU)
Electronic Data and Commands
Processed Data
Command
Component
Key
Raw Data
RC Command
Signals from/to Stock Hardware

## Slide 28: Software Test & Integration Status
Item | Signal Type | Individual simulated test | Individual Hardware Test | Integration and Test | Time Remaining
 | PWM |  |  |  | 
 | f Modulation |  |  |  | 
 | SPI |  |  |  | 
 | PWM |  |  |  | 
 | On/Off |  |  |  | 
 | On/Off |  |  |  | 
 | On/Off |  |  |  | 
 | RS-232 |  |  |  | 
Complete
Complete
5 Hours Remaining
RPM
TEMP
Starter Motor
Pump
Solenoid
Glow Plug
Flow Control
RC Command
Electronic Data and Commands
Predicted 92 Hours, Spent 60
Complete
Complete
Complete
Complete
Complete
Jan 1 8hr Remain Mar 7

## Slide 30: Testing Architecture & Presentation Progress
Fully integrated engine test
Mock engine test with hardware
LabView Engine Simulator Test
ECU/ESB Construction
Seal & Flow
Rate Checks
Lubrication Flowrate Data Collection
ECU/ESB
Chip Tests
ECU Function Development
Level 1
Drive mechanical components with ECU/ESB
Level 3
Level 2
MSR
TRR
Spring Break
April 20
Electrical
Software
Mechanical
Verification Test
Engine Functions With Methane
Engine simulation with Labview
ECU/ESB Construction
ECU/ESB
Chip Tests
Complete
Project Overview
Mechanical
Software and Electronic
Budget
Engine Integration
Notes: This is our baseline design

## Slide 31: Electrical/Software: Command Flow
Student Engine Control Unit
(ECU)
RPM
TEMP
Student Engine Sensor Board
(ESB)
Starter Motor
Pump
Solenoid
Glow Plug
RC Command
RPM Sensor
Thermocouple
Starter Motor
Pump
Solenoid
Glow Plug
Methane Delivery System
Flow Controller
Injectors
Processed Data
Command
Component
Key
Raw Data
Electronic Data and Commands
Signals from/to Stock Hardware

## Slide 32: LabView Simulation Test
Goal: Verify CPRs 3-8 are met in a simulated environment without danger to the engine
Performed in a computer lab
Student Engine Control Unit
(ECU)
RPM
TEMP
Student Engine Sensor Board
(ESB)
Starter Motor
Pump
Solenoid
Glow Plug
RC Command
RPM Sensor
Thermocouple
Starter Motor
Pump
Solenoid
Glow Plug
Flow Controller
Processed Data
Command
Component
Key
Raw Data
Electronic Data and Commands
Signals from/to Stock Hardware

## Slide 33
RPM Sensor
Thermocouple
Starter Motor
Pump
Solenoid
Glow Plug
Flow Controller
Goal: Verify CPRs 3-8 are met in a simulated environment without danger to the engine
Performed in a computer lab
Full Engine Simulator Test

## Slide 34
Signals from/to stock hardware | Expected Signal | Acceptable
 | 0-2400Hz (0-144,000 RPM) | Simulated
 | 0-41mV (0-1000oC) | Simulated
 | 0-8V PWM, 555kHz, 39% Duty Cycle | ±0.5V, ±5kHz ±1% Duty Cycle
 | 0.5V | ±0.01V
 | 10V | ±1V
 | 10V | ±1V
 | RS-232 ASCII From ECU | <3% Baud Rate Error
Full Engine Simulator Test
Mar 9 25hr Remain Mar 23
RPM Sensor
Thermocouple
Starter Motor
Pump
Solenoid
Glow Plug
Flow Controller
Wait For User Command
Engine Running Control Loop
Startup
Emergency Shutdown
Shutdown
Engine Run Sequence
Goal: Verify CPRs 3-8 are met in a simulated environment without danger to the engine
Performed in a computer lab

## Slide 35: Testing Architecture & Presentation Progress
Integrated Engine Test
LabView Engine Simulator Test
ECU/ESB Construction
Seal & Flow
Rate Checks
Lubrication Flowrate Data Collection
ECU/ESB
Chip Tests
ECU Function Development
Level 1
Drive mechanical components with ECU/ESB
Mock Engine Test
Level 3
Level 2
MSR
TRR
Spring Break
April 20
Electrical
Software
Mechanical
Verification Test
Engine Functions With Methane
Drive mechanical components with ECU/ESB
Mock Engine Test
Project Overview
Mechanical
Software and Electronic
Budget
Engine Integration
Notes: This is our baseline design

## Slide 36: LabView Simulation Test
Goal: Verify CPRs 3-8 are met in a simulated environment without danger to the engine
Performed in a computer lab
Student Engine Control Unit
(ECU)
RPM
TEMP
Student Engine Sensor Board
(ESB)
Starter Motor
Pump
Solenoid
Glow Plug
RC Command
RPM Sensor
Thermocouple
Starter Motor
Pump
Solenoid
Glow Plug
Flow Controller
Processed Data
Command
Component
Key
Raw Data
Electronic Data and Commands
Signals from/to Stock Hardware

## Slide 37: Mock Engine Test
Goal: Verify CPRs 3-8 are met using engine hardware without danger to the engine
Performed with air at Boulder Municipal with a blast tunnel
Student Engine Control Unit
(ECU)
RPM
TEMP
Student Engine Sensor Board
(ESB)
Starter Motor
Pump
Solenoid
Glow Plug
RC Command
RPM Sensor
Thermocouple
Starter Motor
Pump
Solenoid
Glow Plug
Methane Delivery System
Flow Controller
Pressure Vessel
Electronic Data and Commands
Processed Data
Command
Component
Key
Raw Data
Run as in engine operation
Not Connected to each other or the engine
Signals from/to Stock Hardware

## Slide 38: Mock Engine Test
RPM Sensor
Thermocouple
Starter Motor
Pump
Solenoid
Glow Plug
Flow Controller
Goal: Verify CPRs 3-8 are met using engine hardware without danger to the engine
Performed with air at Boulder Municipal with a blast tunnel

## Slide 39: Mock Engine Test
Signals from/to stock hardware | Expected Operation | Passing Operation Range
 | 0-2400Hz (0-144,000 RPM) | Simulated
 | 0-41mV (0-1000oC) | Simulated
 | Results TBD | Results TBD
 | On/Off | On/Off
 | 0.9-4.2 g/s | ±5% commanded rate
Mar 20 40hr Remain Apr 4
RPM Sensor
Thermocouple
Starter Motor
Pump
Solenoid
Glow Plug
Flow Controller
Wait For User Command
Engine Running Control Loop
Startup
Emergency Shutdown
Shutdown
Engine Run Sequence
Goal: Verify CPRs 3-8 are met in a simulated environment without danger to the engine
Performed with air at Boulder Municipal with a blast tunnel

## Slide 40: Testing Architecture & Presentation Progress
Engine simulation with Labview
Mock engine test with hardware
ECU/ESB Construction
Seal & Flow
Rate Checks
Lubrication Flowrate Data Collection
ECU/ESB
Chip Tests
ECU Function Development
Level 1
Drive mechanical components with ECU/ESB
Level 3
Level 2
MSR
TRR
Spring Break
April 20
Electrical
Software
Mechanical
Verification Test
Engine Functions With Methane
Engine Functions With Methane
Project Overview
Mechanical
Software and Electronic
Budget
Engine Integration
Fully integrated engine test
Notes: This is our baseline design

## Slide 41: Mock Engine Test
Goal: Verify CPRs 3-8 are met using engine hardware without danger to the engine
Performed with air at Boulder Municipal with a blast tunnel
Student Engine Control Unit
(ECU)
RPM
TEMP
Student Engine Sensor Board
(ESB)
Starter Motor
Pump
Solenoid
Glow Plug
RC Command
RPM Sensor
Thermocouple
Starter Motor
Pump
Solenoid
Glow Plug
Methane Delivery System
Flow Controller
Pressure Vessel
Electronic Data and Commands
Processed Data
Command
Component
Key
Raw Data
Run as in engine operation
Not Connected to each other or the engine
Signals from/to Stock Hardware

## Slide 42: Integrated Engine Test
Goal: Successful operate engine with methane; Verify all requirements (CPR 1-8)
Performed with methane at Boulder Municipal with a blast tunnel
Student Engine Control Unit
(ECU)
RPM
TEMP
Student Engine Sensor Board
(ESB)
Starter Motor
Pump
Solenoid
Glow Plug
RC Command
RPM Sensor
Thermocouple
Starter Motor
Pump
Solenoid
Glow Plug
Methane Delivery System
Flow Controller
Combustor
Electronic Data and Commands
Processed Data
Command
Component
Key
Raw Data
Signals from/to Stock Hardware

## Slide 43
 | Engine Process | Data Collected | Performance Characterization
Objective 1 | Startup | RPM | Maintain engine speed above 35kRPM?
Objective 2 | Shutdown & Emergency Shutdown | Shutdown & Emergency Shutdown | Engine shuts down safely
Objective 3 | Engine Running | RPM & Temperature | Below 130,000 RPM Temperature below 700oC
Objective 4 | Engine Running | Temperature, & Mass Flow Rate | Flow Rate vs Temperature
Apr 25hr Remain Apr 19
Wait For User Command
Engine Running Control Loop
Startup
Emergency Shutdown
Shutdown
Engine Run Sequence
Integrated Engine Test
Goal: Successful operate engine with methane; Verify all requirements (CPR 1-8)
Performed with methane at Boulder Municipal with a blast tunnel

## Slide 44: Critical Project Requirements
Requirement | Subsystem | Description
CPR.1 | FDS | The FDS shall deliver 0.9-4.2g/s ± 5% of methane to the combustion chamber
CPR.2 | FDS | The FDS shall deliver lubricant to the bearings at rates equal to or greater than stock rates
CPR.3 | ESB | The ESB shall read data from the existing thermocouple and hall effect sensor
CPR.4 | ESB | The ESB shall transmit sensor data to the ECU
CPR.5 | ESB | The ESB shall drive signals to engine hardware components
CPR.6 | ECU | The ECU shall implement open loop control to control fuel flow rate
CPR.7 | ECU | The ECU shall shutdown the engine should the exhaust temperature exceed 700oC or the RPM exceed 130,000
CPR.8 | ECU | The ECU shall detect an ignition failure, shutoff fuel flow, and drive compressor
Project Overview
Mechanical
Software and Electronic
Budget
Engine Integration
Notes: This slide is temporary. Just for verify the critical project requirement

## Slide 45: BUDGET
Project Overview
Mechanical
Software and Electronic
Budget
Engine Integration
Notes: This is our baseline design

## Slide 46: Budget – MSR Recap
Chart: 
| ECU | FDS | Testing | Other
Already Spent (MSR) | 265.56 | 2697.22 | 149.27 | 111.2
Remaining (MSR) | 700 | 350 | 900 | 100
Total: $4,273

## Slide 47: Budget – TRR Status
Chart: 
| ECU | FDS | Testing | Other | Remaining Available
Already Spent | 516.78 | 2945.33 | 149.27 | 192.19 | 1196.43
Expected Future Expenses | 740 | 200 | 0 | 300
Total: $5,044

## Slide 48: Budget – TRR Remaining
Chart: 
| Future Costs
ECU, FDS, Other Expected | 1240
Remaining Available | 1196.43

## Slide 50: BACKUP SLIDES
Notes: This is our baseline design

## Slide 51: Methane: Delivery Verification (Detail)
Goal: Verify methane delivery within error bounds (CPR 3)
Shutoff Solenoid
Mass Flow Controller
Check Valve
Pressure Relief Valve
Fuel Injectors
Methane Cylinder
Pressure Vessel
Relief Valve at operational engine pressure
Manual Control
Flowrate Delivered

## Slide 52: Thermocouple Input Software Test
Connect SPI interface to pins C4 throughC7
  Temperature transmitted through SPI bus from ESB
  Interrupt based.
  Runs continuously
EGT used to regulate engine safety – 700o max
Feb 20 2 Hours Remaining Feb 28

## Slide 53: Mass Flow Controller Output Software Test
Connect through RX/TX on pins C2, C3
  Mass flow data transmitted via RS-232 communication protocol
  Function based
  Runs only when called
Mass flow used to control the engine throttle level
Feb 20 2 Hours Remaining Feb 28

## Slide 54: RC Controller Software Test
Connect RC Receiver to pin D3
  D3 – RC Throttle Input
  Interrupt Based
Throttle input used to set the mass flow controller
Feb 20 2 Hours Remaining Feb 28

## Slide 55: RPM Input Software Test
Connect RPM input to pin A6
  Interrupt based
  Must run continuously
RPM used to regulate engine safety – 130,000 max
RPM used to regulate the lubrication flow
Feb 20 2 Hours Remaining Feb 28

## Slide 56: Starter Motor Output Software Test
Connect starter motor to pin E0
  Starter motor receives PWM signal
  Interrupt based
  Runs continuously
Starter Motor used to start the engine, as well as safely cool engine in shut down
Feb 20 2 Hours Remaining Feb 28

## Slide 57: Electrical/Software: Command Flow
Jan 1 5hr Remain Feb 22
Student Engine Control Unit
(ECU)
RPM
TEMP
Student Engine Sensor Board
(ESB)
Starter Motor
Pump
Solenoid
Glow Plug
RC Command
RPM Sensor
Thermocouple
Starter Motor
Pump
Solenoid
Glow Plug
Methane Delivery System
Flow Controller
Injectors
Processed Data
Command
Component
Key
Raw Data

## Slide 58: Electrical/Software: Integrated Testing Part 1
Goal: Verify Engine Sensor Board reads and transmits engine status (CPR.8)
Jan 1 5hr Remain Feb 22
RPM
TEMP
Student Engine Sensor Board
(ESB)
Simulated Input:
Function Generator
DC Power Supply
LabView
Recorded Output:
Oscilloscope
LabView
RPM Sensor
Thermocouple
Processed Data
Command
Component
Key
Raw Data

## Slide 59: Electrical/Software: Integrated Testing Part 2
Goal: Verify Engine Control Unit receives data and sends commands (CPR.X)
Jan 1 5hr Remain Feb 22
Starter Motor
Pump
Solenoid
Glow Plug
RC Command
RPM
TEMP
Student Engine Control Unit
(ECU)
Flow Controller
Processed Data
Command
Component
Key
Raw Data

## Slide 60: Electrical/Software: Integrated Testing Part 3
Goal: Verify Engine Control Unit functions with Engine Sensor Board (CPR X)
Jan 1 5hr Remain Feb 22
RPM
TEMP
Student Engine Sensor Board
(ESB)
Starter Motor
Pump
Solenoid
Glow Plug
RC Command
Student Engine Control Unit
(ECU)
Flow Controller
RPM Sensor
Processed Data
Command
Component
Key
Raw Data
Thermocouple

## Slide 61: Electrical/Software: Integrated Testing Part 4
Jan 1 5hr Remain Feb 22
RPM
TEMP
Student Engine Sensor Board
(ESB)
Starter Motor
Pump
Solenoid
Glow Plug
RC Command
Starter Motor
Pump
Solenoid
Glow Plug
Student Engine Control Unit
(ECU)
Flow Controller
Goal: Verify Engine Control Unit functions with Engine Sensor Board (CPR X)
RPM Sensor
Processed Data
Command
Component
Key
Raw Data
Thermocouple