## Slide 1: RAppelling Cave Exploration Rover
Advisor:
James Nabity
Test Readiness Review
Customer:
Barbara Streiffert
Notes: 15 seconds

## Slide 2: PROJECT STATEMENT
Overview
Test Readiness
Budget
Schedule
This project encompasses designing, building and verifying a rappelling child rover (CR). The CR adds the capability of rappelling to the JPL legacy rover projects and will integrate with the TREADS Mother Rover (MR).
RACER Mission
Rappelling
Returning
Positioning
Exploring
90° Surface
To a maximum depth of 5m
Maximum distance of 5m out
Ground Station (GS) controls motion and imaging
Scattered rocks no larger than 3cm diameter
Depth within +\-10cm
Horizontal distance traveled within +\-10cm
Return to and
re-dock with MR
Notes: 30 seconds

## Slide 3: CONOPS
0) Arrival
- Child Rover
(CR) on MR
1) Deployment (5 min)
- CR undocks
- CR enters cave/pipe
COMMANDS
DATA
TETHER
2) Rappelling (15 min)
- CR rappels 5m
- Transitions from
vertical  horizontal
10cm diameter POI
3) Exploration (120 min)
- CR traverses 5m
- CR takes/stores
image of POI
0) Arrival
- Child Rover
(CR) on MR
NOTE: If comm is dropped during exploration, the CR will be retracted by the MR winch system, after the GS operator says ‘OK’, until comm is restored or CR reaches top of cave/pipe
4) Return (15 min)
- CR is retracted by
MR winch system
5) Re-docking (5 min)
- CR re-enters MR bay
RACER Mission Timeline:
5
15
120
15
5
20
RACER Mission Duration: 160 min Margin: 20 min TOTAL: 180 min
TREADS Mother Rover (MR)
GROUND STATION (GS)
Margin
1
Overview
Test Readiness
Budget
Schedule
2
3
4
5
GS operator has direct line-of-sight view for navigation
After command from GS, rappel is autonomous with feedback loop from CR range-finder
CR movement controlled by GS operator input
Images from CR imaging system used for navigation
NOTE: The return and comm dropout retraction will only continue to approximately the location of the start of Phase 2, based on the range-finder and winch encoder, respectively
Anticipate transmitting ~100 images in the 3hr mission

## Slide 4: CRITICAL PROJECT ELEMENTS
Project Element | Subsystem Breakdown | Rationale | Level of Success
Rappelling | Winch and Drivetrain | The CR shall have the capability to rappel up to 5 m into a cave/pipe | 1
Driving | Chassis, Wheels, and Motors | The CR shall have the ability to explore 5m out from the dropdown point on floor of cave/pipe | 1, 2
Software/Electrical | Microcontrollers, Range Finder, Encoders, Xbees, Imaging, PCB and Batteries | The software will integrate functionality and provide: Accurate position tracking Communication and command protocols Power analysis | 2, 3
Driving
Software/Electrical
Rappelling
Back and Forward Motion
Tether
Scattered Rocks
Overview
Test Readiness
Budget
Schedule
Notes: 30 seconds

## Slide 5: DESIGN OVERVIEW
46cm
46cm
Rappelling Tether
7x19 Braided Steel
Only provides physical connection
MR
CR Wheels
18cm diam., Nitrile rubber treads
Front pair powered for driving/turning
Back pair free for odometry
CR Comm System
2mW 2.4GHz XBee Radio
5dBi dipole antenna
GS
Driving Motors
Original
0.53Nm Faulhaber DC Motors
134:1 internal gear-box
Imaging System
720p Raspberry Pi Cam
Pan/tilt servos and LED light panel
MR Comm System
2 x 2mW 2.4GHz XBee Radios
Serves as relay between GS&CR
GS Comm System
2mW 2.4GHz XBee Radio
Transmits commands from user
Fixed Rappelling
Attachment Point
Zinc-plated steel U-bolt
CR Mass: 7 kg
MR Rappelling System
Custom Winch
15.1 Nm Stepper Motor
Positioning: Depth
Ultrasonic Range Finder
Positioning: Distance Travelled
Two Optical Encoders: Back Wheels
Two Hall Effects Encoders: Front Wheels
CR Power System
Original
Custom Power Distribution PCB
Driving Motors
Updated
0.35Nm Polulu DC Motors
70:1 internal gear-box
CR Power System
Updated
12V CUI Inc. COTS Power Distribution
5V CUI inc. COTS Power Distribution
Overview
Test Readiness
Budget
Schedule

## Slide 6: POST-MSR DRIVING MOTOR UPDATE
Faulhaber motors had too high of a detent torque
  Wheels could not free-spin during rappel or return  requires extra software complexity
Needed a cheap, readily available
1-1 replacement
  Must meet torque requirements & have low detent torque
 | OLD: Faulhaber Motor | NEW: Pololu Motor | Needed
Operational Torque | 18.4 Nm | 0.35 Nm | .33 Nm
Stall Torque | 73.7 Nm | 1.41 Nm | 1.3 Nm
Detent Torque | Unable to test (>>1.85 Nm) | 0.2 Nm | < 1.85 Nm
Software Complexity | High | None | Low
Overview
Test Readiness
Budget
Schedule
Pololu
Faulhaber

## Slide 7: POST-MSR POWER UPDATES
Power regulation system failed Level 1 testing (DR6.1, DR6.2 – Electrical levels and loads)
  Output voltage was 40% lower than designed
  Output voltage was not constant over discharge of battery
Debugging was unsuccessful: alternate solution was needed to meet schedule constraints
SOLUTION: Purchase COTS power regulation components
Component | Meets Design Requirements | Level Testing | Input Sensitivity Testing | Static Load Testing | Dynamic Load Testing | EMC | Efficiency
LM25085AMY/NOPB (Prev. Design) | YES | FAIL | FAIL | FAIL | TBD | YES | PASS
TPS563209DDCT (Prev. Design) | YES | FAIL | FAIL | INCONCLUSIVE | TBD | YES | PASS
PYB30-Q24-S12-U (COTS) [12V] | YES | PASS | PASS | PASS | TBD | YES | PASS
PYB15-Q24-S5-T (COTS) [5V] | YES | PASS | PASS | PASS | TBD | YES | PASS
Overview
Manufacturing
Budget
Schedule
12V
5V

## Slide 8: POST-MSR POSITIONING UPDATE
Overview
Manufacturing
Budget
Schedule
Orientation Vector
CR
Path
CR Odometry:
  By comparing pulses from 4 encoders: can track distance travelled and changes in CR orientation
    Sends this information to GS every second while driving
  Driving over rocks is also detected by comparing encoder pulses
    Forward CG causes both wheels on a side to raise which causes detectable changes in encoder readings
Calculations done on the GS:
  Integrates small changes in orientation and distance traveled to estimate and plot position.
Maximum deviation allowed for return:
+/- 4.3°
FUTURE WORK

## Slide 9: FUNCTIONAL BLOCK DIAGRAM
CR
MR
An Arduino Mega serves to replace the non-functional MR C&DH
Controller
A Raspberry Pi SBC performs C&DH for the CR
Another Arduino Mega interfaces with peripherals except for imaging
Overview
Test Readiness
Budget
Schedule
Notes: 30 seconds – 1 minute

## Slide 10: LEVELS OF SUCCESS
Overview
Test Readiness
Budget
Schedule
Level 1 | 
Level Criteria | Status
The CR shall be able to undock/re-dock to the TREADS CR bay | Needs to be Tested
The CR shall be able to rappel/ascend a 90 degree incline to a max depth of 5m | Needs to be Tested
The CR Shall be able to transition from traversing a vertical to horizontal surface and vice versa | Needs to be Tested
The CR shall be able to take and transmit/store at least 5 images | Demonstrated
Level 2 | 
Level Criteria | Status
The CR shall be able to traverse up to 5m from the rappel touchdown point, controlled via the GS | IN PROGRESS
The CR shall able to resolve a 10cm diameter object from a distance of 5m using the imaging system | Demonstrated
The CR shall provide adequate scene lighting | Demonstrated
The imaging system shall have azimuthal and elevation angular coverage of 180 and 90 degrees | Demonstrated
Level 3 | 
Level Criteria | Status
The CR shall know its depth within the cave/pipe accurate to +/- 10 cm | IN PROGRESS
The CR shall know its horizontal distance travelled accurate to +/- 10 cm | Demonstrated
The CR shall be able to return to the MR at the conclusion of a mission | Needs to be Tested
The CR shall handle communication dropouts with the MR/GS | Needs to be Tested
Currently confident in achieving Levels 1 & 2 for project
  Remainder of Level 1 will be demonstrated within the next 2 weeks
Testing of Comm. dropout protocol will determine if Level 3 success can be met
ACHIEVABLE
FURTHER WORK NEEDED

## Slide 11: WORK PLAN AT MSR
Week 1
Week 5
Week 10
Week 15
Critical Path at MSR followed manufacturing and integration
Legend
= Integration
= Testing
= Software
= Class Milestone
= Internal Milestone
= Manufacturing
Overview
Test Readiness
Budget
Schedule
Notes: 60s

## Slide 12: WORK PLAN POST-MSR
Basic Integration and Component Testing were extended due to further delays with PCB
Now have specific Subsystem-Level Testing tasks with their scheduling based on priority
Critical Path still follows integration, and testing is becoming more critical
NOTE: Uncertainty is included in all task lengths
Week 1
Week 5
Week 10
Week 15
Legend
= Integration
= Testing
= Software
= Class Milestone
= Internal Milestone
= Manufacturing
Overview
Test Readiness
Budget
Schedule
Notes: 60s

## Slide 13: VERIFICATION AND VALIDATION SCHEDULE
Week 10
CR driving functionality is required for all remaining subsystem testing except for power
3/1/2015
Week 5
Week 15
Legend
= Testing
= Class Milestone
= Internal Milestone
Imaging subsystem has been fully verified
Power testing with COTS modules is expected to be relatively fast
Expecting to start full-system validation within the next 3 weeks
Overview
Test Readiness
Budget
Schedule
Notes: 60s

## Slide 14: TESTING OVERVIEW
Completed Tests:
  Small-scale Rappelling Test
In Progress Tests:
  Driving Test
Future Tests:
  System Validation
  Full Scale Communication Drop-out
GS
MR winch and electronics system mounted to platform
CR
1m
2m
3m
4m
5m
GS
CR
Rappelling
Driving
Overview
Test Readiness
Budget
Schedule
Overall: 34%
Percent of Requirements Verified
Most critical for minimum levels of success. Includes Rappelling and Driving

## Slide 15: SMALL-SCALE RAPPELLING TEST OVERVIEW
Tether
Video Camera to record descent progress
GS
Overview
Test Readiness
Budget
Schedule
CR descends at ~10cm/s for most of the rappelling distance
CR will stop at desired depth of
-140cm
Proportional control starts 20 cm above target depth
MR winch and electronics system mounted to platform
140 cm
Rappel distance
EXPECTED RESULTS:
Test Purpose: Verify rappelling control law model
Requirements Verified:
  DR.3.1 – The CR shall be able to rappel vertical slopes
  DR.4.1.1 - The CR shall know its depth within ± 10cm
Test Procedure: MR winch is mounted at top of the wall, the GS sends a command to rappel, track progress with camera, and measure final distance rappelled
Expected Results: Descent follows control law model and is within ± 1cm of actual distance (allowed ± 10cm)
CR descends at ~10cm/s for most of the rappelling distance
GS
EXPERIMENTAL SETUP:
MR WINCH SYSTEM
1.8m Wall
CR CHASIS

## Slide 16: SMALL-SCALE RAPPELLING TEST: RESULTS
Proportional descent-rate control is enabled as CR approaches the target depth:
- DR.3.1: ✔
- Model Verification: ✔
CR stops at the appropriate depth for the front wheels to be touching the ground
Reference distances in background of video used to track CR position over time
CR rappelled to within +/-0.5cm of target and stopped:
- DR.4.1.1: ✔

## Slide 17: SMALL-SCALE RAPPELLING TEST: RESULTS
Proportional descent-rate control is enabled as CR approaches the target depth:
- DR.3.1: ✔
- Model Verification: ✔
CR stops at the appropriate depth for the front wheels to be touching the ground
Reference distances in background of video used to track CR position over time
CR rappelled to within +/-0.5cm of target and stopped:
- DR.4.1.1: ✔
- Model
Verification: ✔
Error bars for depth computed from assuming +/- 10 pixel accuracy in position tracking
Error bars for descent rate calculated from positional error and timing error added in quadrature

## Slide 18: DRIVING TEST - OVERVIEW
Positional Error Over Mission Duration, cm
Overview
Test Readiness
Budget
Schedule
1m
2m
3m
4m
5m
After each command, the distance travelled by the CR will be measured and compared with CR odometry
Required to know distance travelled within +/- 10cm over the mission duration
Must miscount fewer than 18.1 encoder pulses per meter driven to meet requirement
GS
Procedure: Incrementally drive forward 1m up to 5m, measure distance travelled and compare to encoders. Repeat when driving backwards to simulate full mission distance
Expected Results: <10cm of error over the mission duration (<1cm average error per meter driven)
  Maximum of 18 average miscounted pulses per meter driven allowable
Test Purpose: Verify driving performance and horizontal distance travelled positioning accuracy
Requirements Verified:
  DR.3.3 – The CR shall be able to traverse a distance of up to 5m horizontally from the rappel touchdown point
  DR.4.1.2 - The CR shall know its distance travelled within ± 10cm

## Slide 19: DRIVING TEST – PRELIMINARY RESULTS
Preliminary testing has demonstrated basic functionality with driving forward
  CR can be commanded to drive a distance
Current status:
  Encoder pulses are not being counted accurately
  Average error per meter driven is too high to meet requirement
Future work:
  Start removing possible sources of error:
    Wheel slip from testing on a slick surface
    Gear ratio of motors may be different from what is advertised
    The CR overshoots its target because of its momentum
  Perform additional testing with driving backwards and turning
Overview
Test Readiness
Budget
Schedule
See large positive bias between how far the CR thinks it has travelled and how far it really has
Magnitude of bias is not consistent between trials
Would result in a negative bias

## Slide 20: SYSTEM VALIDATION - OVERVIEW
Test Purpose: Validate the overall system as it performs the mission
Test Location:
  South ITLL Patio
Systems to be Validated:
  Driving – FR.3: The CR shall explore a cave or pipe
  Rappelling – FR.3: The CR shall explore a cave or pipe
  Positioning – FR.4: The CR shall contain a positioning system
  Imaging – FR.5: The CR shall capture photographic images
  Power – FR.6: The CR and MR systems shall contain their own electrical power systems
  Software – FR.7: The CR, MR, and GS systems shall be controlled with software
CR
GS
MR
Overview
Test Readiness
Budget
Schedule
Notes: Can we be more specific about which ITLL patio. Like west patio possibly
And re-ordering of the systems

## Slide 21: SYSTEM VALIDATION – TEST ENVIROMENT
Overview
Test Readiness
Budget
Schedule
Concrete
MR Platform
Rappelling Stage:
Positional data at end of rappel to validate model
Expected result: within 1cm of actual depth
Transition is Pass/Fail
Exploration Stage:
Positional data throughout driving
  Recorded by test operators through openings in side of “pipe”
Expected result: within 10cm of actual distance travelled over the course of this stage
5m plywood “pipe”
Scattered rocks less than 3cm in diameter
5m Vertical Surface
2
3
1) Deployment (5 min)
- CR undocks
- CR enters cave/pipe
2) Rappelling (15 min)
- CR rappels 5m
- Transitions from
vertical  horizontal
3) Exploration (120 min)
- CR traverses 5m
- CR takes/stores
image of POI
4) Return (15 min)
- CR is retracted by
MR winch system
5) Re-docking (5 min)
- CR re-enters MR bay
ITLL South Patio To Scale:
Deployment Stage:
Pass/Fail
1
Return Stage:
Positional data recorded as before for distance travelled and depth
Expected results: within 10cm for distance, within 1cm for depth
4
Re-docking Stage:
Pass/Fail
5
1m
1m
Notes: Is this slide for the overall system validation?

## Slide 22: Full Scale Comm. Drop-Out Verification
Overview
Test Readiness
Budget
Schedule
Concrete
MR Platform
5m plywood “pipe”
5m Vertical Surface
1m
1m
Test Purpose: Verify comm. drop-out protocol in full test environment
Requirements Verified:
  DR.7.2.1.1 – The CR will implement communication drop-out protocol
Start location of CR
Test Procedure:
  Case 1 – Comm. is not restored and CR is reeled in to start of Rappel phase
  Case 2 – Comm. is restored prior to complete reel in
Case 2 end location
Case 1 end location
Notes: Is this slide for the overall system validation?

## Slide 23: BUDGET UPDATE
Overview
Test Readiness
Budget
Schedule
Spending Category | Money Spent ($)
Miscellaneous & Shipping | 510
Imaging | 142
Power | 684
Software | 150
Rappelling | 766
Driving | 1187
Communication | 251
Money Spent | 3690
Remaining Budget | 1310
Have budget left for duplicates of any critical components
All procurements for 1 rev. of project have been purchased
Expect to spend less than CDR projected budget of $4500
Remaining expenses: report printing, test environment supplies (wood and rocks), cable management supplies, etc.

## Slide 24: SUMMARY OF FUTURE WORK
Overview
Test Readiness
Budget
Schedule
Level 1 | 
Level Criteria | Status
The CR shall be able to undock/re-dock to the TREADS CR bay | Needs to be Tested
The CR shall be able to rappel/ascend a 90 degree incline to a max depth of 5m | Needs to be Tested
The CR Shall be able to transition from traversing a vertical to horizontal surface and vice versa | Needs to be Tested
The CR shall be able to take and transmit/store at least 5 images | Demonstrated
Level 2 | 
Level Criteria | Status
The CR shall be able to traverse up to 5m from the rappel touchdown point, controlled via the GS | IN PROGRESS
The CR shall able to resolve a 10cm diameter object from a distance of 5m using the imaging system | Demonstrated
The CR shall provide adequate scene lighting | Demonstrated
The imaging system shall have azimuthal and elevation angular coverage of 180 and 90 degrees | Demonstrated
Level 3 | 
Level Criteria | Status
The CR shall know its depth within the cave/pipe accurate to +/- 10 cm | IN PROGRESS
The CR shall know its horizontal distance travelled accurate to +/- 10 cm | Demonstrated
The CR shall be able to return to the MR at the conclusion of a mission | Needs to be Tested
The CR shall handle communication dropouts with the MR/GS | Needs to be Tested
Further work includes full-system validation as well as some subsystem-level verification
  Must demonstrate undocking/re-docking, full rappelling and return, and transitions
ACHIEVABLE
FURTHER WORK NEEDED
By 3/23
By 3/23
By 3/8
By 3/23
By 3/23
By 3/8
By 3/8

## Slide 25: QUESTIONS?

## Slide 26: PRELIMINARY DRIVING TEST

## Slide 27: CRDriveState Class
Overview
Testing
Budget
Schedule
CRDriveState{
private:
depth
orientation
distanceTraveled
prevBackLeftDistance
prevBackRighttDistance
prevFrontLeftDistance
prevFrontRightDistance
state
checkEncoders()
public
getCRDriveState()
setCRDriveState()
- Other getters and setters.
}
Encapsulates all CR state variables into a single object.
Keeps track of the previous distances on each wheel.
Introduces the “state” variable
  See Next Slide
checkEncoders() uses new encoder data and previous wheel distances to determine changes in state, distance traveled, and orientation.
  Will be used in main drive loop.

## Slide 28: CR State
Integer variable that represents a driving condition (rocks, slip, etc..)
Assumes a forward CG
State | Name | Conditions
0 | RAPPELLING | Ignore encoder readings (disableInterrupts)
1 | DRIVING | No anomalies. Average all encoder readings.
2 | ROCK_FRONT_LEFT | FL > FR, FR ≈ BR, RL ≈ 0
3 | ROCK_FRONT_RIGHT | FR > FL, FL ≈ RL, BR ≈ 0
4 | ROCK_FRONT_ALL | FR ≈ FL, BR ≈ BL, FL > BL, FR > BR
5 | ROCK_REAR_LEFT | FL ≈ FR, BL > BR,
6 | ROCK_REAR_RIGHT | FL ≈ FR, BR > BL,
7 | ROCK_REAR_ALL | FR ≈ FL, BR ≈ BL, FL < BL, FR < BR
8 | SLIP_FRONT_LEFT | FL > FR, FR ≈ BR ≈ BL
9 | SLIP_FRONT_RIGHT | FR > FL, FL ≈ BR ≈ BL
10 | SLIP_FRONT_ALL | FR ≈ FL, BR ≈ BL ≈ 0

## Slide 29: IMAGE RESOLUTION TEST
10cm Object
Requirements Verified:
  DR.5.1 – Imaging system shall have a minimum resolution of 3.7 pixels per degree of field of view in a single image
  DR.5.4 – The imaging system light source shall provide adequate lighting to determine a POI from background
Test Purpose: Verify scene lighting and image resolution requirements
Test Procedure: Room light was turned off, LED light panel was turned on, and image was captured
5m
Horizontal distance
Test Location: Lockheed Martin Room
Systems Tested: Imaging, Communication, and Software
Overview
Testing
Budget
Schedule

## Slide 30: POWER SYSTEM DEBUGGING
Switches at correct frequency, but always 50% duty cycle
Changing voltage on feedback pin doesn’t change output
Any change to input voltage changes output

## Slide 31: PERFORMANCE OF NEW POWER COMPONENTS
PYB30-Q24-S12-U (12V)
  This encompasses the entire discharge profile of the battery and meets our level requirements
  Line regulation of 0.1%
PYB15-Q24-S5-T (5V)
  This encompasses the entire discharge profile of the battery and meets our level requirements
  Line regulation of 0.1%
 | 12 V Regulation | 5 V Regulation
No Load | 11.941 +/- 0.002V | 5.015 +/- 0.001V
Full Load | 11.941 +/- 0.015V | 5.015 +/- 0.006V
Input voltage range (As Advertised) | 8.2V-36V | 8.2V-36V

## Slide 32: MOTOR DRIVER & RESPONSE TO SMALL PWM INPUT SIGNAL
PWM duty cycle: <2%
  Motor fully powered off
PWM duty cycle: 2-3.1%
  Motor detent torque decreased
PWM duty cycle: >3.1%
  Motor freely rotating
This shows we can partially power the motors without them moving to allow the rover to be more easily pulled backward.

## Slide 33: TORQUE – SPEED PLOT
Faulhaber Motor Performance
Pololu Motor Performance
Faulhaber (Red) & Pololu (Blue) Motor Performance

## Slide 34: Requirements Verified
Requirement | Description | Verification method | Result
DR.1.1 | The CR shall fit within the TREADS CR bay | Child requirements met | N/A
DR.1.1.1 | The CR shall have an area footprint no greater than 0.483m x 0.483m | Inspection | Footprint – 0.46m x 0.46m
DR.1.1.2 | The CR shall have a mass of no more than 9.8 kg | Inspection | Mass – 7 kg
DR.1.3 | The winch subsystem shall fit onto the MR | Child requirements met | N/A
DR.1.3.1 | Additions to the MR structure shall not exceed 10 kg | Inspection | Mass – 6.5 kg
DR.2.1 | The CR shall receive commands from the GS via the MR relay system | Inspection | Command sent from GS was received at CR
DR.2.1.3 | The CR shall receive commands to take a picture and store the image | Testing | CR took/stored image at command of GS
DR.2.2 | The CR shall be able to transmit images to the GS via the MR | Inspection | Image taken from CR was received at GS
DR.2.2.1 | Transmission shall be a minimum of 18 bits/min baud rate per pixel in an image | Testing | Send image in 29s, required to do so in 108s

## Slide 35: Requirements Verified cont.
Requirement | Description | Verification method | Result
DR.3.1 | The CR shall be able to rappel vertical slopes | Testing | As seen in main presentation
DR.4.1.1 | The CR shall know its depth within +/- 10cm | Testing | Within +/- 1cm
DR.5.1 | The imaging system shall have a minimum resolution of 3.7 pixels per degree of field of view in a single image | Testing | 1 image equals 23.9 x 17.4 pixel per degree of field of view
DR.5.4 | The imaging system light source shall provide adequate lighting to determine a POI from background | Testing | See imaging test back up slide
DR.5.5 | The CR shall be able to store at minimum of 5 images | Demonstration | 5+ images were taken and stored on SD card
DR.7.1.2 | The CR software shall command the imaging system to take an image and save onboard | Testing | See imaging test back up slide
DR.7.4 | The MR software shall be able to interpret commands from MR communication system | Testing | Commands were successfully carried out by MR software (Rappelling)
DR.7.8 | The GS software will display the image upon receiving from the MR relay and save to the GS | Testing | See imaging test back up slide

## Slide 36: BUDGET ITEMIZATION – Test/Misc.

## Slide 37: BUDGET ITEMIZATION – Comm./Power/SW

## Slide 38: BUDGET ITEMIZATION – Driving

## Slide 39: BUDGET ITEMIZATION – Driving cont./ Rappelling

## Slide 40: BUDGET ITEMIZATION – Power

## Slide 41: BUDGET ITEMIZATION – Power cont.