## Slide 1: I2CE TRR
Group 12
Sponsored by: ASTROBi
Notes: Brady Kopec, Kate Boykin, Lila Monprode, Reid Schneckenburger, Joe Miserlian, Jack Huston, Skylar Clark, Ben Esser, Ryan Bennett
Stuff the PDR needs to address:
• What is the purpose of the project and what are its specific objectives (measures of success)?
• What is the proposed design solution, and how does it work?
• What are the critical project elements for meeting the success criteria?
• What are the associated design requirements and how does the design satisfy them? Note: requirements at this time should have discrete values; for example ‘The spacecraft shall operate at a 44 gHz uplink.’ Or ‘The end of the robot arm shall deflect no more than 3 mm in the negative xdirection’
• What are the remaining risks and their mitigations?
• How will the design be verified and validated?
• How is the remaining work organized?

## Slide 2
Skylar Jack Reid Joe Brady Kate Ben Ryan Lila
Schedule
Overview
Test Readiness
Budget

## Slide 3: Overview

## Slide 4: Project Definition
This project is to design and fabricate a proof-of-concept sensor capable of measuring the plume density of ice particles around Enceladus
Schedule
Overview
Test Readiness
Budget

## Slide 5
Schedule
Overview
Test Readiness
Budget

## Slide 6: Primary Objectives
Measure incident particle flux over time
2) Detect particles from 0.5 μm to 4 μm in radius​
3) Operate in vacuum conditions
~1,000 – 1,000,000 times smaller
4) Develop Parametric Model to predict sensor performance
Schedule
Overview
Test Readiness
Budget
Notes: Kate

## Slide 7: Higher Level Objectives
Measure the speed and charge of particles of radius > 0.5 μm
I2CE
60
60
Measure particles with an incidence angle of 60 from sensor opening (120 total FOV)
Schedule
Overview
Test Readiness
Budget
Notes: Kate

## Slide 8: CPEs
Geyser Density Detection
  Measure particles per second incident to the spacecraft
  Used to prove that the spacecraft is flying through ice plume
Noise Mitigation
  Must reduce external noise
  Maximize usable data
Simulation
  Must quantitatively model the sensor response to incident ice particles
Schedule
Overview
Test Readiness
Budget
Notes: Kate

## Slide 9: Final Design Solution
Copper Mesh
-Good electrical properties
Copper Wool
-Captures incident particles
Aluminum
-Creates faraday cage
Insulating Material
-Prevents shorting of sensor
-Provides isolation
ICE Particles
Schedule
Overview
Test Readiness
Budget
Notes: 10x10x10 cm
- we broke up our sensor into two main components- an electrostatic conduction and electrostatic induction apperatus.
-Copper wool is essentially steel wool made out of copper. This helps capture the incident particles. The mesh will be soldered on to the faraday cup.
-The aluminum case and external copper meshes (entry and exit of sensors) will create a faraday cage that isolates the electrical circuit and sensing grids within the box from external electrical noise.
-0.5-4 micrometers

## Slide 10: Design Updates from CDR
Major
  New induction sensing grid attachment method
  Updated grid mesh density
Minor
  New electrical components
    Resistors, capacitors, etc.
Schedule
Overview
Test Readiness
Budget

## Slide 11
Schedule
Overview
Test Readiness
Budget

## Slide 12: Schedule
Schedule
Overview
Test Readiness
Budget

## Slide 13: Tests to be Performed
 | Complete Tests | Incomplete Tests
Component | ADC testing Manufacturing capability Electronics component verification | 
Subsystem | Convolution with accurate timing Direct charge on Breadboard ADC  Raspberry Pi communications test PCB functional verification | Faraday cage verification Thermal assurance test Vacuum compatibility
System | Direct charge injection Open Air Induction PCB Vacuum Conduction PCB | Direct charge injection Open air test Vacuum chamber test (day in the life)
Schedule
Overview
Test Readiness
Budget
Notes: Kate

## Slide 14: Semester Schedule
Schedule
Overview
Test Readiness
Budget

## Slide 15: Test Schedule
Schedule
Overview
Test Readiness
Budget

## Slide 16: Test Readiness
Schedule
Overview
Test Readiness
Budget

## Slide 17: Test #1: Direct Charge Application
Schedule
Overview
Test Readiness
Budget

## Slide 18: Testing Overview
Purpose
  Test the basic functionality of each PCB
  Create a calibration curve relating charge/voltage
Overview
  Expected charge is directly injected into the PCB via function generator
    Applying voltage across capacitor gives specified amount of charge
  Variation: Oscilloscope / Integrated System DAQ
    ADC and Raspberry Pi functionality
Schedule
Overview
Test Readiness
Budget

## Slide 19: Testing Rationale – Requirements to be Verified
Data Acquisition
Electronics
1.2.1: Shall filter out external noise
1.2.2: Shall send data in useable packets to human readable format
1.2.4: Sensor sampling rate shall be sufficient to capture required frequencies
2.2.4: System shall be capable of detecting and measuring transducer output
MO.3 : Minimize effects of noise
Schedule
Overview
Test Readiness
Budget
Notes: Define what we mean by SNR and noise

## Slide 20: Critical Pre-requisite Testing
Electronics
Component
Verification
Breadboard
Direct
Charge
ADC & Raspberry Pi
Communications Test
PCB
Functional Verification
Schedule
Overview
Test Readiness
Budget

## Slide 21: Definition of Success
Pass/Fail Criteria
  Success:
    Receive a signal out
    Detect events
  Failure:
    Sensor output does not react to input charge
    Output voltages are not unique for a given input charge
    System SNR is too low for valid testing
Expected Performance Results
 | Open Air - Conduction | Open Air - Induction | Vacuum - Conduction | Vacuum - Induction
Input Charge | 86 pC / s | 18pC | 86 pC / s | 0.5fC
Voltage Output | 4V | 2V | 4 V | 4V
Schedule
Overview
Test Readiness
Budget

## Slide 22: Model Validation
Expected relationship between input charge and output voltage
  same shape as the input charge
Can compare expected signal with measured signal
Schedule
Overview
Test Readiness
Budget
t1
t2
t3
t4
time
charge

## Slide 23: Model Validation
Schedule
Overview
Test Readiness
Budget

## Slide 24: Model Validation
Calculate speed for particle with known speed
  Use shape and edges of signal
Compare calculated vs. input
Schedule
Overview
Test Readiness
Budget
Actual | 1 m/s
Calculated | 0.962 m/s
Percent Error | 3.8%

## Slide 25: Scope – Test Setup
  Power Supply
  Wave Generator
  Oscilloscope
  Grounded Faraday Cage
  ESD mat and wrist strap
  With integrated DAQ
    Digital signal output as .csv file
  Without integrated DAQ
    PCB probed at test point
    Routed to oscilloscope and saved to .csv or equivalent
Equipment
Data Acquisition
Schedule
Overview
Test Readiness
Budget

## Slide 26: Scope – General Test Procedure
Connect PCB to
  Power Supply
  Wave Generator
  Oscilloscope / Raspberry Pi
Place PCB inside of grounded faraday cage
Verify connections and grounds
Input desired charge signal
Collect Analog / Digital Data
Remove that
Schedule
Overview
Test Readiness
Budget

## Slide 27: Reducing Risk
Signal to Noise Ratio Too Low
Risk Level
High
Low
Schedule
Overview
Test Readiness
Budget
Before Direct Charge Application
After Direct Charge Application
Notes: After performing test, SNR will be meaningful enough to get significant, accurate data -> defined by pass criteria of test

## Slide 28: Test #2: Open Air Test
Schedule
Overview
Test Readiness
Budget

## Slide 29: Testing Overview
Purpose
  Verify intersystem compatibility
    Mechanical system relays signal to the open-air PCB
    Digital signal is recorded via Raspberry Pi
  Verify velocity estimation algorithm
Overview
  Small water droplets are released above the sensor
    Variation of heights / velocities
    Test does not depend on droplet size
  Droplets transfer charge to sensor
  Electronics will amplify and convert this charge to a voltage
Schedule
Overview
Test Readiness
Budget
Notes: Qualitative not quantitative verification

## Slide 30: Testing Rationale
Test Design
Data Acquisition
1.1.1.1: Sensor shall detect presence of incident charged particles
3.1.2: Conduction section shall detect particles from 0 to 60 degrees incident angle
1.2.1: Shall filter out external noise
1.2.2: Shall send data in useable packets to human readable format
3.5.1: Shall receive data from sensor and perform input signal analyses to determine particle characteristics at 10 Hz
MO.1: Sensor shall detect particles
Schedule
Overview
Test Readiness
Budget

## Slide 31: Critical Pre-requisite Testing
Schedule
Overview
Test Readiness
Budget
Direct Charge Injection
Direct Charge Pre-Reqs
Faraday Cage Verification

## Slide 32: Definition of Success
Pass/Fail Criteria
Success:
  Signal output shape matches model
  Sensor accepts all particles within 60 incident angle
Failure:
  No signal detected
  Results do not meet expected performance
Expected Performance Results
  Conduction: Stair Step / Linear Increase
  Induction: Trapezoid
Schedule
Overview
Test Readiness
Budget
Notes: Whoever does this slide needs to understand how/why the expected results are the same but for a different reason
Not directly imputing a trapezoid, but assuming that’s what the result of a particle impact should owlook like
Happens because of physics (charge induction and charge transfer for conduction)

## Slide 33: Scope – Test Setup
  Pipette
  Clamps
  Water
  Ruler
  Video recording device
Data Acquisition
Equipment
  Raspberry Pi
    Connected to sensor via D-Sub
    Connected to master computer via ethernet
  Computer
Schedule
Overview
Test Readiness
Budget
Notes: LOGGER PRO!!!!!

## Slide 34: Scope – Test Procedure
Mount sensor and pipette
Set up camera to record water falling
Drop water droplets into sensor
  Induction: Five testing heights, ten drops each
  Conduction: Five testing heights, ten drops each, test angles at ±60° in two axes of rotation
Record data via Raspberry Pi
Schedule
Overview
Test Readiness
Budget

## Slide 35: Reducing Risk
Cannot Detect Individual Particles
Risk Level
High
Low
Schedule
Overview
Test Readiness
Budget
Before Open Air Test
After Open Air Test

## Slide 36: Test #3: Vacuum Chamber Test
(Day in the Life)
Schedule
Overview
Test Readiness
Budget

## Slide 37: Testing Overview
Purpose
  Verify sensor can detect particles with similar charge and speed like those found around Enceladus
Overview
  Particles will be given a charge equivalent to particles around Enceladus
  Particle launcher will be used to accelerate particles at induction and conduction sensors
  Results will be read and processed by the Raspberry Pi outside the vacuum chamber
Schedule
Overview
Test Readiness
Budget

## Slide 38: Testing Rationale
Vacuum Compatibility
1.1.3: Shall be electrically compatible to the vacuum chamber
1.1.4: Shall be physically compatible to the vacuum chamber
1.1.5: Shall be able to dissipate all heat that is generated
MO.4: Perform vacuum chamber test
Enceladus Environment
1.1.1.2: Sensor shall detect presence of incident charged particles of sizes 0.5 to 4 micrometers
1.1.2: Sensor shall react to incident particles with relative velocities from 100 to 300 m/s
Schedule
Overview
Test Readiness
Budget

## Slide 39: Critical Pre-requisite Testing
Open Air Test
Vacuum Compatibility
Thermal Assurance Test
Schedule
Overview
Test Readiness
Budget

## Slide 40: Definition of Success
Pass/Fail Criteria
Success:
  Sensor reacts to particle flux
Failure:
  Sensor does not react to particle flux
  PCBs overheats/fails
Expected Performance Results
Induction Sensor: Detects charge and speed of particles within +/- 10%
Conduction Sensor: Detects charge flux of particles within +/- 10%
Schedule
Overview
Test Readiness
Budget

## Slide 41: Scope – Test Setup
Equipment
Data Acquisition
Completed sensor
Vacuum Chamber & Particle Launcher
Power Supply
Wire Harnesses & Cables
  Raspberry Pi
    Connected to sensor via D-Sub
    Connected to master computer via ethernet
  Computer
Schedule
Overview
Test Readiness
Budget

## Slide 42: Scope – Test Procedure
Confirm safe arrival of components
Place the sensor within the vacuum chamber
Assemble & connect wire harnesses
Ensure conduction sensor is aligned with particle launcher
Power on Raspberry Pi and confirm communication with sensor
Pull vacuum and begin particle launch procedure with data collection
Repeat steps 4-7 for induction sensor
Schedule
Overview
Test Readiness
Budget

## Slide 43: Reducing Risk
Cannot Detect Particles of Expected Charge
Risk Level
High
Low
Schedule
Overview
Test Readiness
Budget
Before Vacuum Chamber Test
After Vacuum Chamber Test

## Slide 44: Budget
Schedule
Overview
Test Readiness
Budget

## Slide 45: Budget Overview
Total Budget | + $4000.00
CU Toolbox Safety Deposit | - $200.00
Previous Project Spending | -$1871.34
Future Spending | -$1030.00
Remaining Margin | +$898.66
Schedule
Overview
Test Readiness
Budget

## Slide 46: Previous Spending
Chart: 
| Electronics | Computing | Mechanical
Column1 | 1005.8 | 286.93 | 578.63
Schedule
Overview
Test Readiness
Budget
Mechanical
$578.61
30.9%
Electronics
$1005.80
53.7%
Computing
$286.93
15.3%
Subsystem | Amount
Electronics | $1005.80
Computing | $286.93
Mechanical/Manufacturing | $578.61
Total Spent | $1871.34

## Slide 47: Future Spending & Margin
Items | Amount :
PCB Iterations (5) | -$430
Electronics Margin | -$200
Shipping & Insurance | -$400
Total | -$1030
Undesignated Remainder: | $898.66
Schedule
Overview
Test Readiness
Budget
Chart: 
| PCBs | Electronics | Shipping & Insurance | Margin
Sales | 430 | 200 | 400 | 898.66
Margin
$898.66
46.6%
PCB Iterations
$430.00
22.3%
Elec. Margin
$200.00
10.4%
Shipping & Insurance
$400.00
20.7%

## Slide 48: Final Budget
Chart: 
| Electronics | Future Electronics | Mechanical | Computing | Shipping/Insurance | CU Safety Deposit | Margin
Sales | 1005.8 | 630 | 578.61 | 286.93 | 400 | 200 | 898.66
Schedule
Overview
Test Readiness
Budget
Electronics
$1005.80
25.1%
Future Electronics
$630
15.8%
Computing
$286.93
7.2%
Shipping & Insurance
$400
10%
CU Safety Deposit
$200
5%

## Slide 49: Thank you for listening!
Special thanks to:
Advisor: Dr. Erik Knudsen
Sponsor: Erik Buehler & ASTROBi Foundation
Course Coordinators: Dr. Kathryn Wingate & Chris Muldrow
Lab Directors: Trudy Schwartz, Bobby Hodgkinson, Matt Rhode, Nate Coyle
Dr. Zoltan Sternovsky
The Senior Project Advisory Board

## Slide 50: Backup Slides

## Slide 51: Functional Requirements
1.1: The sensor shall detect amplitude of incident ice particles over time.
1.2: The sensor shall relate amplitude to particle size for a given speed.
1.3: The sensor shall operate in near perfect vacuum conditions.
1.4: The sensor shall dissipate no more than 10W power.
1.5: The sensor shall determine the average impact rate of ice particles.
1.6: The sensor shall determine individual particle charge.
1.7: The sensor shall fit within the provided vacuum chamber.
1.8: The team shall develop a parametric model for predicting the real response of the ice particle impact dynamics on the incident surface

## Slide 52: CSA – Impact of Faraday Cage
Noise Mitigation Implementation

## Slide 53: Event Detection - Convolution
Threshold
Notes: Joe

## Slide 55: Charge Based Sensing
Particles have an inherent, measurable charge
Combination of two charge detection methods:
Purpose & Objectives
Design Solution
Requirements & Satisfaction
CPE's & Risks
Project Planning
Verification & Validation
Electrostatic Conduction | Induction
Best for bulk charge Heritage: Parker Solar Probe, Cassini | Best for large, individual particles Heritage: Cassini
Notes: Detailed discussion on differences between Conduction and Induction sensing?
Why are we using induction if conduction meets our requirements? It helps us characterize the velocity and size of the larger particles we encounter. This is important as larger particles will be more likely to contain frozen single cell organisms that Astrobi is concerned with.

## Slide 56: Charge Based Sensing - Conduction
Conduction Based – Faraday’s Cup
Incident particles impact sensor face, some charge is transferred
Sensor face is discharged periodically
Cannot measure individual particles
  Measures total charge density
Conduction
Ice Particles
Purpose & Objectives
Design Solution
Requirements & Satisfaction
CPE's & Risks
Project Planning
Verification & Validation

## Slide 57: Charge Based Sensing - Induction
Induction Based – Mesh Grid
  Negatively charged particles fly through a conductive wire grid
  Particles induce a charge in the grid
  Measurements of integrated electrons show particle charge
Measures speed
Purpose & Objectives
Design Solution
Requirements & Satisfaction
CPE's & Risks
Project Planning
Verification & Validation
Notes: Do not talk about induced current, talk about induced charge in the mesh grid. This is what the charge sensitive amplifier measures.
-Talk aobut electrostatic physics
-Why do we car about

## Slide 58: Circuit Specifications
 | Open Air - Conduction | Open Air - Induction | Vacuum - Conduction | Vacuum - Induction
Input Charge | 50 18pC particles (0.9nC) | 18pC | 100 0.5fC particles (50fC) | 0.5fC
Stages | Charge Sensitive Amplifier (CSA) Low Pass Filter | CSA Low Pass Filter | CSA Low Pass Filter | CSA Band Pass Filter Voltage Amplification
Filter + Voltage Amplification | 2 Stage Gain = 0 | 1 Stage Gain = 0 | 2 Stage Gain = 400 | 1 Stage Gain = 100 + Secondary Gain of 400
Voltage Output | 4.09V | 2V | 4 V | 4V
 | Open Air - Conduction | Open Air - Induction | Vacuum - Conduction | Vacuum - Induction
Input Charge | 50 18pC particles (0.9nC) | 18pC | 100 0.5fC particles (50fC) | 0.5fC
Stages | Charge Sensitive Amplifier (CSA) Low Pass Filter | CSA Low Pass Filter | CSA Low Pass Filter | CSA Band Pass Filter Voltage Amplification
Filter + Voltage Amplification |  |  |  | 
Voltage Output | 4.09V | 2V | 4 V | 4V
Notes: FOCUS on the differences without going into detail on each box
Difference between Open Air and Vacuum tests to be detailed later

## Slide 59: PCB Functional Block Diagram
Two PCBs inside the vacuum chamber
D-Sub leads to and from the Raspberry Pi
Each PCB will have a Vacuum and Open-Air Design
  4 total PCBs designed

## Slide 60: Filter Creation
Anti-Aliasing / Lab Noise filtering
Final Design | Open Air | Vacuum
Induction | Low Pass 1 Stage Gain = 0 | Band Pass 1 Stage Gain = 100
Conduction | Low Pass 2 Stages Gain = 0 | Low Pass 2 Stages Gain/Stage = 20
Final Design | Open Air | Vacuum
Induction |  | 
Conduction |  | 

## Slide 61: Vacuum Circuit Schematics
Note: All grounds are tied
Induction Circuit
Conduction Circuit
Notes: Have only CSA circuit (everything else in backup), have conduction and induction side by side on same slide

## Slide 62: Open Air Test - Conduction Circuit
Note: All grounds are tied

## Slide 63: Open Air Test - Induction Circuit
Note: All grounds are tied

## Slide 64: Power Regulation Circuits
Identical Power Regulation on all PCBs
3.3V Regulator
  7.5V input from voltage divider stage of 5V regulator

## Slide 65: Electronics Testing

## Slide 66: CSA Testing- Component Information
Trial 1 - 1 μC
Circuit Values | 
Vin | 1 V
R | 120 kΩ
C1 | 1 μF
C2 | 22.5 μF
Circuit Values​ | 
Vin​ | 5 mV​
R​ | 220 MΩ​
C1​ | 10 pF ​
C2​ | 10 pF ​
Trial 3 – 50fC
Circuit Values | 
Vin | 50 mV
R | 220 MΩ
C1 | 10pF
C2 | 10pF
Trial 2 – 0.5pC

## Slide 67: Mesh Grid
More sensitive to smaller particles than individual electrodes
  Less sensitive than tube
Wide range of impact angles
Flight Heritage - Cassini

## Slide 68: Key Requirement: Incident Angle
Sensor shall detect particles with incident angles between 0 and 60 degrees
  0 degrees is defined as perpendicular to the sensor plate
Conduction section geometry will capture all particles in this range
60°
1.2 in.
0.693 in.

## Slide 69: Sampling Frequency Models

## Slide 70: Sensor Stray Capacitance
Capacitance of sensor relates to sensor noise
  Should be less than 8 pF according to Dr. Zoltan Sternovsky who has designed similar detectors
Sensor acts as two capacitors in parallel
Due to Miller Effect this capacitance is virtually grounded and does not affect measurement, just contributes to noise
3 cm
3 cm
Per Sensing Plane:
Total:

## Slide 71: Risk Matrix Criteria - Probability
What is the Probability the Risk Will Happen? |  | 
Level 1 | Not Likely | Avoid or mitigate risk with standard practices
Level 2 | Low Likelihood | Create plan to mitigate risk with minimal oversight
Level 3 | Likely | Workarounds must be applied to mitigate associated risk
Level 4 | Highly Likely | Cannot mitigate this type of risk, different approach may be successful
Level 5 | Near Certainty | Cannot mitigate this type of risk, no workarounds available

## Slide 72: Risk Matrix Criteria - Impact
Given the Risk is Realized, what would be the Magnitude of Impact? |  |  | 
Level | Technical | Schedule | Cost
1 | Minimal or no impact | Minimal or no impact | Minimal or no impact
2 | Slight alterations required | Minor slip in schedule, remains within margin | Slight increase in budget
3 | Components must be altered or added | Additional activities required to recover | Serious impact on budget plans
4 | Unacceptable, but workarounds available | Impact on program critical path | Little to no margin remaining in budget
5 | Unacceptable, no alternatives exist | Cannot meet major program milestone | Budget exceeds allowable amount